## Slide 1
RES PROJECT - FEDERAL OFFICE OF CIVIL PROTECTION (FOCP) - Conception Phase
    Preliminary results
      8th of March 2024
Notes: Welcome to this presentation. First of all, I would like to thanks Nicolas Wyrsch and his team for the opportunity to present this project. My name is .. I am professor @ HES-SO Valais-Wallis, my lab is specialized in integrating IT technologies to help and accelerate the energy transition and I am teaching software architecture, systems integration and software industrialization @ HES-SO Sierre. Today, I am representing 3 HES-SO research teams : Prof. Francesco Termine and his team @HE-Arc, Prof Julien Pouget with Dr. Baoling Guo @HES-SO Valais-Wallis and my team with Gwenaële Gustin who implemented the simulation tool that we will see later.

## Slide 2
How could the electrification of the mobility and V2X mitigate the electricity shortage/power system failures?
1. Introduction
2. Critical infrastructure needs
3. Methodology, pre-analysis of local network capacity
4. GIS simulation tool: visualisation and simulation of electrical scenarios

## Slide 3
1. Introduction

## Slide 4
Power shortages vs. power system failures
The terms are often confused, but do not mean the same thing.
Hardly a day goes by without the terms «power system failure» and «power shortage» being used in the media.
Despite the fact that they do not mean the same thing, the terms are often mixed up or used synonymously.
Let’s clear up any confusion:
Source : https://www.swissgrid.ch/en/home/newsroom/blog/2022/power-shortages-vs-power-system-failures.html

## Slide 5
Power shortages
As the term indicates, if a power shortage occurs, there is a lack of electrical energy in the system.
Existing production capacities are therefore insufficient to meet the demand. In its national risk analysis «Disasters and Emergencies in Switzerland» in November 2020, the Federal Office for Civil Protection considered power shortages to be the greatest risk faced by Switzerland, with serious consequences for economy and society.
The risk increases towards the end of winter.
Source : https://www.swissgrid.ch/en/home/newsroom/blog/2022/power-shortages-vs-power-system-failures.html
Test lab HES-SO @ Swiss Digital Center, Sierre

## Slide 6
Power system failures
In contrast to a power shortage, during a power system failure there is usually enough energy available to meet demand.
However, a chain of unfortunate circumstances means that the energy can no longer be transported from the power plant to consumers.
If, for example, a natural event causes grid elements to fail, this can result in other elements being overloaded. These are then automatically disconnected.
Source : https://www.swissgrid.ch/en/home/newsroom/blog/2022/power-shortages-vs-power-system-failures.html

## Slide 7
Worldwide blackout referencing (in progress)
Location | Year | Duration | No. of people | Causes
Marseille | 2023 | 10h | 6'000 | Cold and overload
Var and Alpes-Maritimes | 2023 | A few hours | 750'000 | Usage overload
Texas | 2021 | A few days | 4,500,000 households | Storms
Japan | 2011 | More than a month | 2,600,000 households (165,000 households still affected, on 02.04.2011) | Earthquake
Italy | 2003 | A few hours | 57,200,000 (whole country) | Outage of HV lines in Switzerland and France (suppliers, domino effect)
USA-Canada | 2003 | 2 weeks (max.) | 55'000'000 | Usage overload
USA-Canada | 1998 | 45 days (max.) | Several million | Storms and ice
France | 1999 | 19 days | 3'600'000 | Storms

## Slide 8
Feedback from blackouts around the world (in progress)
Problem areas
Health
Strong presence in emergency departments and significant need for equipment
Risk of spoilage of vaccines due to loss of refrigeration
Environment
Contamination of natural water compared with wastewater
Increase in the number of rodents linked to the increase in the number of perishable foodstuffs thrown away
All areas
Falling emergency generators
Loss of data from the syndromic surveillance system (public health monitoring)
Difficulty sterilising hospital equipment
Difficulty processing waste
Increase in food and heat-related illnesses
Service in place | Actions implemented and issues addressed
Logistics and information systems | Packaging vaccines and managing the storage of essential pharmaceutical products
Medical and clinics | Opening of cooling centers Needs assessment for the most vulnerable people (elderly and mental health) in collaboration with organisations that manage social housing Visiting and helping vulnerable people
Epidemiology and surveillance | Syndromic surveillance activities maintained Assessment of the effects of the blackout on health (e.g. heat stroke)
Environment | Assessing and maintaining water potability Revision of water supply plans envisaged, should the blackout continue
Public and information provider | Communication through radio and newspapers on good behaviour (e.g. throwing away out-of-date food)
Laboratory | Air filter testing for environmental monitoring
Mental health | Maintenance of the emergency call service (fax number that uses less power than the digital number)

## Slide 9
Vehicle-to-grid potential in Switzerland
Ref: Van Liedekerke, A., M. Schwarz, and G. Blazhe. "Vehicle-to-grid in Switzerland, A first estimate of the value of vehicle-to-grid for the Swiss electricity system." ETH Zürich, 18th February (2023).

## Slide 10
2. Critical infrastructure needs

## Slide 11
Critical infrastructure needs
  1. Detailed interviews with stakeholders (producers, consumers, electricity network operators)
    Interviews with users
    Interviews with producer
    Interviews with the network manager
  2. Integration of new data into the data collection tool (with possible modification of the data model)
  Data exchange process with Viteos
  3. Management of data protection contracts for each site selected
  Drafting and signing a data use agreement with critical users to obtain their consumption data

## Slide 12
Purpose of the interviews
Understanding the decision-making chain
Identification of current blackout management practices, including strategies, preparations and responsibilities
Identifying the obstacles and risks associated with governance
Outline potential solutions, taking into account current and future technological capabilities

## Slide 13
3. Methodology,
pre-analysis of local network capacity

## Slide 14
Step 0: During a blackout, critical consumers transit into auto-consumption mode using backup battery or gas generator within a short time.
Step 1: Islanded microgrids Identification, the microgrids can ensure the supply of critical consumers for longer duration by profiting local production and storage units within their domain.
Concept and Methodology
Ref: Ferrari, M., Ollis, B., Starke, M., & Massol-Deya, A. (2023). The Well-Connected Microgrid: A Network of Microgrids can Withstand Severer storms. IEEE Spectrum, 60(10), 36-43.
V2G
V2G
V2G
V2G
New opportunities of V2G: increasing resilience in shortage, blackout, extreme events.
Notes: To identifier microgrid in Step 1:
- Maximum use of the current grid network infrastructure
- The local production (PV, hydro, biomass, generator, ) should at least ensure the balance of the critical loads within their domain.
- Storage units can be considered to increase the resillence …

## Slide 15
Concept and Methodology
Step 1: Identify islanded microgrids that can ensure the supply of critical consumers for longer duration by profiting local production and storage units within their domain.
Step 2: Networking the microgrids together, allowing them to share resources and makes them more resilient during blackout.
Ref: Ferrari, M., Ollis, B., Starke, M., & Massol-Deya, A. (2023). The Well-Connected Microgrid: A Network of Microgrids can Withstand Severer storms. IEEE Spectrum, 60(10), 36-43.
New opportunities of V2G: increasing resilience in shortage, blackout, extreme events.

## Slide 16
  - Investigate the microgrid solution supported with distributed productions (PVs, hydropower, etc.), storage batteries, and EVs (V1G, V2G, V2X) via providing grid-support services (step 1 + step 2).
  - Investigate the detection methodologies for both unintentional and intentional islanding modes.
  - Define load-shedding rules and protections following the load priorities.
  - Assess critical vulnerabilities within communication systems susceptible to cyberattacks.
  - Digital Twin development and hardware-in-the-loop validation, ensuring that the tests are efficient, streamlined and representative of the actual environment in the demonstrator.
Technical development
Methodology development
Social Science research
  - Map critical loads in the order of priority with the engagement of relevant stakeholders in Neuchâtel.
  - Investigate the motivations of energy communities (micro-grid) to provide flexibility to increase grid resilience in shortage, blackout, and extreme events (extreme hot, cold, flood).
  - Investigate the motivations of the EV users (V1G, V2G, V2X) via providing EVs batteries storage capacity for resilience enhancement by using the concept of emergency demand response programs.
  - Evaluate policies and regulations that could encourage end-users and demand response program.
Notes: We innovatively combined the inspired studies implementing insights from a Social Sciences and Humanities and the technical research in this project.

## Slide 17
Case study: Blackstart capabilities of WWTP Neuchâtel
Waste Water Treatment Plant, WWTP Neuchâtel is motivated to participate in energy transition and resilience enhancement in the near future.
Source: https://step-ne.ch/

## Slide 18
Case study: Blackstart capabilities of WWTP Neuchâtel
Energy self-sufficiency and complementarity in 2025, source: https://STEP-ne.ch/documents/publications/Pr%C3%A9sentation%20Fran%C3%A7ais__2022.pdf
Notes: The aim of the new energy production facilities is to maintain self-production despite the new nitrogen and micropollutant treatment facilities, which consume more energy.

## Slide 19
Case study: Blackstart capabilities of WWTP Neuchâtel
Self-sufficient operation in 2025, source: https://STEP-ne.ch/documents/publications/Pr%C3%A9sentation%20Fran%C3%A7ais__2022.pdf
Notes: During the day, electricity will be generated by the photovoltaic panels installed on the roofs of the WWTP buildings (already in place) and by the photovoltaic wave (2,000 kWh per day). In addition, by recovering the organic matter extracted from the wastewater (the bacteria that "work" in the digester), the WWTP produces biogas. This biogas, which is normally stored during the day, can also be used to power a generator that supplements this production when needed during the day (4,450 KWh per day). However, the generator is generally shut down during the day.
At night, the WWTP will be able to rely on the biogas released by the bacteria to power the generator, which will supply the electricity needed to keep it running at night. In this way, the WWTP will be self-generating and will even be able to inject a surplus into the Viteos electricity grid.

## Slide 20
4. GIS simulation and visualisation Tool

## Slide 21
Simulation and visualisation tool
Visualization of PV potential and zone selection

## Slide 22
Specification of dataset
date: datetime of exported data
baseMVA: Base power rating of the network
bus:
  base_kv: Base voltage
  coord: Coordinates of the bus
  country: Country of the bus
  index: Index of the bus
  name: Name of the bus
  population: Population assigned to this bus
  status: Status of the bus (0: inactive, 1: active)
gen:
  gen_bus: Bus to which the generator is connected
  gen_status: Status (0: out of service, 1: in service)
  index: Index of the generator
  pg: Active power generated or produceMW (=pg*baseMVA)
  pmax: Active power generation capacity (*baseMVA for MW)
  type: Type of generator
load:
  index: Index of the load
  load_bus: Bus the load is attached to
  pd: Active power consumption or consumeMW (=pd*baseMVA)
  status: Status of the load bus (0: inactive, 1: active)
branch:
  br_status: Status of the branch (0: inactive, 1: active)
  f_bus: Index of the from bus
  index: Index of the branch
  pf: Real power injected at the from bus (*baseMVA for MW)
  pt: Real power injected at the to bus
  rate_a: The thermal rating of the line (*baseMVA for MW)
  t_bus: Index of the to bus
  Transformer: Bool whether the line is a transformer
  Line usage (%): |pf|/rate_a
  Loss: |pf|-|pt|

## Slide 23
HV Network after algorithm treatment
Visualization of HV network and simulation of the line capacities, consumption and production nodes (PanTaGruEl algorithm developed by prof. Philippe Jacquod)
Source: Bachelor Thesis Gwenaëlle Gustin Business IT Course programme HES-SO Sierre https://sonar.rero.ch/hesso/documents/326901

## Slide 24
Simulation and visualisation tool for MV and LV
WWTP production, consumption and grid connections

## Slide 25
Projet in conception phase and next step

## Slide 26
Next phase
Proposition for SFOE P+D project (Pilot and Demonstration programme) that will focus on the pilot area Neuchâtel (discussion with potential partners in progress)
If you are interested, please contact :
Prof. David Wannier, david.wannier@hevs.ch

## Slide 27
Appendix

## Slide 28
Simulation and visualisation tool
  Visualisation of the potential of PV roofs in a selectable area around defined consumers
  Viewing the connection of consumption nodes
  Addition of colour-coded line capacity
  Line activation/deactivation function for different scenarios

## Slide 29
Development in progress
- Check results of MV Network with reality
- Add line capacity calculation (based on documentation transmitted by Vitéos)
- Add link between MT network and production/consumption nodes
- Add activation and deactivation of production/consumption nodes
- Add line activation/deactivation
- Create new algorithm and API to balance network production and consumption
- Integrate Proof-of-concepts to online platform citiwatts.eu

## Slide 30
Simulation tools/methods to choose from:
Simulation tools to choose from | Static model | Dynamic model | Protection rules | Controller design | Simulation mode
Matlab | YES | Establish a dynamic generator/turbine model | The protection functions can be modelled as follows | YES | Offline digital simulation
NEPLAN | YES | NO | Simplified protection | NO | Offline digital simulation
PowerFactory | YES | There are dynamic generator models. | It has protection functions defined in the software. | NO | Offline digital simulation
EMTP | YES | YES | YES | NO | Offline digital simulation
Hardware-in-the-loop simula platform (Opal-RT, Typhoon) | YES | YES, it can run in real-time with real physical component | YES | YES | Real-time simulation
Methodology development
Notes: Dynamic simulations will be carried out using Matlab-Simulink software to assess the behaviour of the machines and their controllers in different islanding scenarios.
Machine and controller models are based on modelling assumptions due to the lack of information.
Matlab/Simulink is a powerful tool for studying islanding (as shown), but it can also be used for faults, protection, etc.
The validation tests use Hardware-In-the-Loop (HIL) laboratory, provided by HES-SO, Valais, emulating grid and other environment components, making sure that the procedure is efficient, streamlined and representative of the actual environment in the potential demonstrators. This step minimizes risks to components, allows the assessment of stability and operational challenges in almost real conditions yet in a controlled environment, and thus facilitates the deployment of the solutions to the future demonstration project .